## Slide 1: Multi-functional Cane An assistive device for the visually impaired
Submitted By:
Ali Yazbeck- 94764
Serena Haidar - 90457
Zein Attar -94266
Approved By:
Dr. Mohamad Shreif
Embedded Design

## Slide 2: Outline
Introduction
Project Objective
Required Components
Circuit Design
Implementation
Conclusion

## Slide 3: Project Objective
Measure the temperature in a specific medium.
Show measurement range between -40C and +125C.
Light up RGB LEDs differently according to the corresponding temperature.

## Slide 4: Problem : Challenges Faced by the Visually Impaired
Detecting obstacles
Navigating unfamiliar environments
Lack of access to affordable smart devices
Safety risks at night or in emergencies

## Slide 5: OUR MOTIVATION
Help blind people navigate their environment in a safer way
Applying embedded systems for social impact
Desire to build practical, accessible solutions

## Slide 6: EXISTING SYSTEMS
Project Name | Object Detection | Audio Feedback | GPS / SMS | Light Safety | Notes
SmartCane (IIT Delhi) | Ultrasonic sensors | Vibration alerts | No | No | Widely adopted; lacks GPS or AI features
Batcane (Leeds University) | Sonar-based echolocation | Vibration alerts | No | No | Detects obstacles in multiple directions; no GPS/audio
XploR Cane (Birmingham City U.) | Facial recognition | Bone-conduction audio | Yes | No | Enhances social interaction; limited recognition range
Chest Camera + Wristbands (US) | Computer vision (obstacles) | Vibrating wristbands | No | No | Effective in crowds; lacks GPS and audio
Our Project | Ultrasonic sensors | MP3 audio alerts | Yes | Yes | Includes water hazard detection, lighting, and emergency SMS

## Slide 7: PROPOSED SOLUTION: MULTI-FUNCTIONAL CANE
SOLUTION
Combine sensors with embedded systems for real-time feedback
Add GPS and emergency functions
Affordable and easy to maintain
Obstacle detection for safer navigation
Light up in the dark for safety
Compass orientation and direction guidance
GOALS
Ensuring a safer navigation
Assisting in the case of emergencies
Enhancing mobility and independence

## Slide 8: FUNCTIONALITY
Obstacle Detection
Voice-Assisted Navigation
Automatic Nighttime Lighting
Emergency Button + Location Sharing
Water Detection

## Slide 9: Required Components

## Slide 10: ARDUINO MEGA 2560 : OVERVIEW
Low-cost and low-power System on a Chip (SoC) microcontroller
Developed by Espressif Systems.
Designed for mobile devices, wearable electronics and Internet of Things (IoT) applications
Wireless Connectivity: Wi-Fi and Bluetooth
Processor speed : 240 MHz
Memory: 520 KiB SRAM and 448 KiB ROM
Supports external flash and PSRAM

## Slide 11: ESP32 : FEATURES
Peripheral interfaces:
  34 programmable GPIOs
  12-bit SAR ADC, DAC, SPI, UART, PWM and more
Clocks and timers:
  2 Internal oscillators (8 MHz and RC) with calibration
  2 External crystal oscillator : 2 MHz ~ 60 (40 MHz only for Wi-Fi/Bluetooth functionality) and 32 kHz for RTC with calibration
Power Management: 5 power modes, including deep sleep(10 μA.) and Hibernation for energy efficient operation.

## Slide 12: Arduino UNO
The Arduino Uno is an open-source microcontroller board based on the Microchip ATmega328P microcontroller and developed by Arduino.cc. The board is equipped with sets of digital and analog input/output pins that may be interfaced to various expansion boards and other circuits.

## Slide 13: MAIN COMPONENTS
DFPlayer
SIM Card + Speaker
Ultrasonic sensor

## Slide 14: MAIN COMPONENTS
LDR + LED
Water sensor
Sensors: Ultrasonic + voice feedback

## Slide 15: COMPONENTS: COMMUNICATION AND LOCATION MODULES
ESP32
NEO-6M GPS Module
Emergency Button

## Slide 16: ESP32 : OVERVIEW
Low-cost and low-power System on a Chip (SoC) microcontroller
Developed by Espressif Systems.
Designed for mobile devices, wearable electronics and Internet of Things (IoT) applications
Wireless Connectivity: Wi-Fi and Bluetooth
Processor speed : 240 MHz
Memory: 520 KiB SRAM and 448 KiB ROM
Supports external flash and PSRAM
Clocks and timers:
  2 Internal oscillators (8 MHz and RC) with calibration
  2 External crystal oscillator : 2 MHz ~ 60 (40 MHz only for Wi-Fi/Bluetooth functionality) and 32 kHz for RTC with calibration

## Slide 17: COMPONENTS: POWER MANAGEMENT
18650 Li-ion Rechargeable Batteries
TP4056 Battery Charging Module
Slide Switch

## Slide 18: COMPONENTS: ADDITIONAL
Breadboard
Jumper Wires
Resistors
Cane and Box

## Slide 19: 16*2 LCD
An LCD is an electronic display module which uses liquid crystal to produce a visible image. The 16×2 LCD display is a very basic module commonly used in DIYs(Do It Yourself) and circuits. The 16×2 translates a display 16 characters per line in 2 such lines. In this LCD each character is displayed in a 5×7 pixel matrix.

## Slide 20: Temperature Sensor [TMP36]
The TMP36 is a low voltage, precision centigrade temperature sensor. It provides a voltage output that is linearly proportional to the Celsius temperature. It also doesn't require any external calibration to provide typical accuracies of ±1°C at +25°C and ±2°C over the −40°C to +125°C temperature range.

## Slide 23: Circuit Design

## Slide 24: Operation
This Device gives the temperature of a certain medium by displaying it on the 16*2 LCD .
The RGB LEDs light correspondingly to the temperature value.

## Slide 25: Implementation

## Slide 26: Code Sample
if(temp<-15.82)
rgbcolor(255,255,255);//when the temperature is less than -15.82 the RGB LED lights pink
else if(temp>82.813)
rgbcolor(255,0,0);//when the temperature is above 82.813 the RGB LED lights red

## Slide 27: Conclusion
This device makes our life easier, safer and more practical by displaying not only the temperature as numerical value, but also a lightning color that corresponds to a specific temperature.
We learned how to apply engineering to create a prototype for a specific system.

## Slide 28: Tinkercad link
https://.....

## Slide 29: Thank you
We are ready to answer your questions